## Slide 2
After this lecture you will be able to
  learn the architecture of OSI model.
  understand the layers of OSI model and their functions.

## Slide 3: Layered Tasks
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.
Topics discussed in this section: Sender, Receiver, and Carrier Hierarchy.

## Slide 4: Tasks involved in sending a letter
The letter is written, put in an envelope, and dropped in a mailbox.
The letter is carried from the post office to the mailbox
The letter is picked up, removed from the envelope; and read
The letter is carried from the mailbox to a post office.
The letter is delivered to a carrier by the post office.
The letter is delivered from the carrier to the post office
Higher layers
Middle layers
Lower layers
The parcel is carried from the source to the destinations
Sender
Reciever

## Slide 5: The OSI Model
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
Topics discussed in this section: Layered Architecture, Peer-to-Peer Processes, Encapsulation.

## Slide 6: OSI Model
OSI is the model
ISO is the organization

## Slide 7: Seven layers of the OSI model
Application
Presentation
Session
Transport
Network
Data link
Physical
1
2
3
4
5
6
7

## Slide 8: The Interaction between Layers in the OSI Model

## Slide 9: An exchange using the OSI model

## Slide 10: Application Layer

## Slide 11: Application Layer

## Slide 12: Application Layer

## Slide 13: Application Layer

## Slide 14: Application Layer

## Slide 15: Application Layer

## Slide 16: Specific Services Provided by the Application Layer
Network virtual Terminal
File transfer, access, and management.
Mail services.
Web Surfing

## Slide 17: Specific Services Provided by the Application Layer
Network virtual Terminal
TELNET

## Slide 18: Specific Services Provided by the Application Layer
File transfer, access, and management.
FTP

## Slide 19: Specific Services Provided by the Application Layer:
Mail services
Sender
Internet
SMTP
SMTP
SMTPPOP3 / IMAP
Sender’s Mail Server
Receiver’s Mail Server
Receiver

## Slide 20: Web Surfing

## Slide 21: NOTE
The application layer is responsible for providing services to the user.

## Slide 22: Presentation Layer
Presentation layer
Application Layer

## Slide 23: Presentation layer
What is the format of data?

## Slide 24: Presentation Layer
Specific responsibilities of the presentation layer includes-
  Translation
  Encryption
  Compression

## Slide 25: Translation

## Slide 26: Translation
101011100011100011000
Convert
Example conversion of ASCII to EBCDIC

## Slide 27: Data compression
Presentation layer used to reduce the data before transmission that is known as Data compression.
That can be Lossy and Lossless compression.

## Slide 28: Data Compression
Data Compression
Lossless Data
Compression
Lossy Data
Compression

## Slide 29: Encryption and Decryption

## Slide 30: Note
The presentation layer is responsible for translation, compression, and encryption.

## Slide 31: Session layer
Dialog Control
Authentication and Authorization
Session management
Synchronization

## Slide 32: Session Layer
Party

## Slide 33: Session Layer
Setting up

## Slide 34: Session Layer
Assisting

## Slide 35: Session Layer
Cleaning

## Slide 36: Same case with Session Layer
Helping to setting up connection
Dialog control

## Slide 37: Same case with Session Layer
APIs NETBIOS
Helping to setting up connection
APIs NETBIOS

## Slide 38: Authentication and Authorization
Authentication
Authorization
Who are you?
What permissions do you have?
VS

## Slide 39: Authentication and Authorization

## Slide 40: Session Management

## Slide 41: Synchronization
System sending a file of 2000 pages

## Slide 42: Synchronization
After 100 pages

## Slide 43: Note
The session layer is responsible for dialog control and synchronization.

## Slide 44: Transport layer
Segmentation and reassembly
Flow control
Error Control
Service point addressing

## Slide 45: Segmentation and Reassembly
Session layer
Transport Layer

## Slide 46: Segmentation and Reaasembly
Session layer
Transport Layer
Data Unit
Data Unit
Data Unit
Segments

## Slide 47: Segmentation and Reassembly
Sequence no. and port number
data unit
Segments
Sequence no. and port number
data unit
Sequence no. and port number
data unit

## Slide 48: Segmentation and Reassembly
Sequence no. and port number
data unit
Sequence no. and port number
data unit
Sequence no. and port number
data unit

## Slide 49: Segmentation and Reassembly
Reassemble segments
Application Layer
Data
Segment 2
Segment 1
Segment 3

## Slide 50: Flow Control
100Mbps
10Mbps
50Mbps

## Slide 51: Error Control
Automatic repeat request
Data Unit
Data Unit
Data Unit
Data Unit
Data Unit
Missing

## Slide 52: Error Control
Automatic repeat request
Data Unit
Data Unit
Data Unit
Data Unit
Data Unit
Checksum
Data Unit
Checksum
Checksum
Checksum
Corrupted

## Slide 53: Protocols of Transport Layer
TCP | UDP
Connection Oriented transmission | Connectionless transmission
TCP is slower | UDP is faster
Acknowledgment | No Acknowledgment
Used where full data delivery is must | Does not matter whether we gave received all data

## Slide 54: Service point addressing
Internet
Network layer
Host-to-host delivery
Transport layer
Process-to-process delivery
Process
Process

## Slide 55: Note
The transport layer is responsible for the delivery of a message from one process to another.

## Slide 56: Network Layer
Logical Addressing
Routing

## Slide 57: Logical Addressing
Transport layer
Network Layer
Segments

## Slide 58: Logical Addressing
Ipconfig command

## Slide 59: Logical Addressing
Transport Layer
Network Layer
Network 1
Network 2
Segment
IP1 IP2
IP 1
IP 2
Packets
Segment
Sender
Receiver

## Slide 60: Routing

## Slide 61: Note
The network layer is responsible for the delivery of individual packets from the source host to the destination host.

## Slide 62: Data Link Layer
Network layer
Data Link Layer
Data Link layer receives data packet from network layer. Data packets contains IP address of sender and receiver.

## Slide 63: Data Link Layer
Framing
Physical addressing
Flow control.
Error control
Access control.

## Slide 64: Physical Addressing
If frames are to be distributed to different systems on the network, DataLink layer adds header to the frame.

## Slide 65: Types of Addressing
Types of Addressing
Physical addressing
Logical addressing

## Slide 66: Types of Addressing
Types of Addressing | 
Logical Addressing | Physical addressing
Done at Network layer | 
Sender and receiver IP addressing are assigned to each segment to form a data packet

## Slide 67: Types of Addressing
Types of Addressing | 
Logical Addressing | Physical addressing
Done at Network layer | Done at Data Link Layer

## Slide 68: Types of Addressing
Types of Addressing | 
Logical Addressing | Physical addressing
Done at Network layer | Done at Data Link Layer

## Slide 69: Types of Addressing
Types of Addressing | 
Logical Addressing | Physical addressing
Done at Network layer | Done at Data Link Layer
Network Interface card
Network Interface card

## Slide 70: Types of Addressing
Local media includes

## Slide 71: Types of Addressing
Local media includes

## Slide 72: Types of Addressing
Local media includes

## Slide 73: Flow Control
Data link layer imposes a flow control mechanism to avoid overwhelming the receiver.

## Slide 74: Error Control
Adds reliability to the physical layer by adding mechanisms
Detect and retransmit damaged or lost frames.
Recognize duplicate frames.
Normally achieved through a trailer added to the end of the frame.

## Slide 75: Access Control
Data link layer keeps an eye when shared media is Free that device can send data. This is called CSMA.

## Slide 76: Note
The data link layer is responsible for moving frames from one hop (node) to the next.

## Slide 77: Physical layer
Transport layer
Network layer
  1000101010101000111000000(Bits)
Signals
Media
Data link layer

## Slide 78: The physical layer is also concerned
Data rate
Synchronization of bits
Physical topology
Transmission mode

## Slide 79: Note
The physical layer is responsible for movements of individual bits from one hop (node) to the next.

## Slide 80: Summary
Application
Presentation
Session
Transport
Network
Data link
Physical
To allow access to network resources
To establish, manage, and terminate sessions
To move packets from source to destination; to provide internetworking
To transmit bits over a medium; to provide mechanical and electrical specifications
To organize bits into frames; to provide hop-to-hop delivery
To provide reliable process-to-process message delivery and error recovery
To translate, encrypt, and compress data

## Slide 81: Protocol Data Unit (PDU)
Data
Application
Presentation
Session

## Slide 82: Protocol Data Unit (PDU)
Data
Application
Presentation
Session
Transport
Segments

## Slide 83: Protocol Data Unit (PDU)
Data
Application
Presentation
Session
Transport
Network
Segments
Packets

## Slide 84: Protocol Data Unit (PDU)
Data
Application
Presentation
Session
Transport
Network
Data link
Segments
Packets
Frames

## Slide 85: Protocol Data Unit (PDU)
Data
Application
Presentation
Session
Transport
Network
Data link
Physical
Segments
Packets
Frames
10101100