## Slide 2
After this lecture, you will be able to
  learn what is transmission media.
  differentiate between wired and wireless media.

## Slide 3: Transmission Medium
Transmission medium and physical layer

## Slide 4: Classes of Transmission Media
Transmission media
Guided (wired)
Twisted-pair cable
Coaxial cable
Unguided (wireless)
Free space
Fiber-optic cable

## Slide 5: Selecting Transmission Media
Transmission rate
Cost and ease of installation
Resistance to environmental condition
Distances

## Slide 6: Guided Media
Wired media are the cables that are tangible or having physical existence.
Bounded transmission media
  Twisted-pair cable
  Coaxial cable
  Fiber-optic cable

## Slide 7: Why to Twist Wires ?
Effect of wire on parallel wires
Noise Source

## Slide 8: Why to Twist Wires ?
One of the wires is used to transmit data and the other is the ground reference
Twisted Wires

## Slide 9: Twisted Pair Cable

## Slide 10
UTP and STP cables
Unshielded Twisted Pair (STP) Cable
Shielded Twisted Pair (STP) Cable

## Slide 11: Category of Cables
CAT3: | Rarely used today, CAT3 is usually deployed in phone lines. It supports 10 Mbps for up to 100 meters.
CAT4 | : Typically used in token ring networks, CAT4 supports 16 Mbps for up to 100 meters
CAT5: | Used in Ethernet-based LANs, CAT5 contains two twisted pairs. It supports 100 Mbps for up to 100 meters.
CAT5e: | Used in Ethernet-based LANs, CAT5e contains four twisted pairs. It supports 1 Gbps for 100 meters.
CAT6: | Used in Ethernet-based LANs and data center networks, CAT6 contains four tightly wound twisted pairs. It supports 1 Gbps for up to 100 meters and 10 Gbps for up to 50 meters.

## Slide 12
UTP connector

## Slide 13: Advantages of Twisting
Reduces crosstalk
It also prevent from external form of signal interference.
Simple
Flexible
Connected
Easy to install and maintain
Low weight
Very cheap

## Slide 14: Advantages of Twisting
Reduces crosstalk.
It also prevent from external form of signal interference
Simple
Flexible
Connected
Easy to install and maintain
Low weight
Very cheap

## Slide 15: Advantages of Twisting
Reduces crosstalk.
It also prevent from external form of signal interference.
Simple
Flexible
Connected
Easy to install and maintain
Low weight
Very cheap

## Slide 16: Advantages of Twisting
Reduces crosstalk.
It also prevent from external form of signal interference.
Simple
Flexible
Connected
Easy to install and maintain
Low weight
Very cheap

## Slide 17: Advantages of Twisting
Reduces crosstalk.
It also prevent from external form of signal interference.
Simple
Flexible
Connected
Easy to install and maintain
Low weight
Very cheap

## Slide 18: Advantages of Twisting
Reduces crosstalk.
It also prevent from external form of signal interference.
Simple
Flexible
Connected
Easy to install and maintain
Low weight
Very cheap

## Slide 19: Advantages of Twisting
Reduces crosstalk.
It also prevent from external form of signal interference.
Simple
Flexible
Connected
Easy to install and maintain
Low weight
Very cheap

## Slide 20: Advantages of Twisting
Reduces crosstalk.
It also prevent from external form of signal interference.
Simple
Flexible
Connected
Easy to install and maintain
Low weight
Very cheap

## Slide 21
UTP and STP cables
foil
Copperwire

## Slide 22: Disadvantages of Twisted Pair Cable
High attenuation(loss in signal) :carrying a signal for large distance without repeater is problem.
Low bandwidth.
Max data rate range from 1MBPS to 10 MBPS without any extra devices.

## Slide 23: Disadvantages of Twisted Pair Cable
High attenuation(loss in signal) :carrying a signal for large distance without repeater is problem.
Low bandwidth.
Max data rate range from 1MBPS to 10 MBPS without any extra devices.

## Slide 24: Disadvantages of Twisted Pair Cable
High attenuation(loss in signal) :carrying a signal for large distance without repeater is problem.
Low bandwidth.
Max data rate range from 1MBPS to 10 MBPS without any extra devices.

## Slide 25: UTP Connector

## Slide 26: Coaxial Cable

## Slide 27: Fill in the Blanks
Coaxial cables are widely used for ______________ connections and ______________________.

## Slide 28: Fill in the Blanks
Coaxial cables are widely used for ______________ connections and ______________________.
Cable TV
LANs

## Slide 29: BNC Connectors

## Slide 30: Performance of coaxial cable

## Slide 31: Categories of Coaxial Cables
Thicker | Thinnet
Coax Cable RG-8 10Base5 Thicknet Cable | Coax Cable RG-58 10Base2 Thinnet Cable (Cheapernet)
Category | Impedance | Use
RG-59 | 75 | Cable TV
RG-58 | 50 | Thin Ethernet
RG-11 | 50 | Thick Ethernet

## Slide 32: Differences between Thicknet and Thinnet
Thicknet | Thinnet
Thicker than thinnet | Thinner
Max length 500 meters | Max length 185 meters

## Slide 33: Advantages of Coaxial cable
Transmission (datarate) much better than twisted.
It can be used as shared cable n/w.
Mainly used for broadband transmission(all channels are on send simltaneously,all channels are on same wire).
High bandwidth -400mbps.

## Slide 34: Disadvantages of Coaxial Cable
Expensive
Not compatible with twisted pair cable

## Slide 35: Fibre Optic Cables
Used in medical equipment

## Slide 36: Fibre Optic Cables
Used in medical equipment
Made up of thousand of fiber strands

## Slide 37: Fibre Optic Cables
Used in medical equipment
Made up of thousand of fiber strands
Single fiber strand is as thin as human hair

## Slide 38: Fibre Optic Cables
Used in medical equipment
Made up of thousand of fiber strands
Single fiber strand is as thin as human hair
Carries information in the form of light

## Slide 39: Fibre Optic Cable
It consist of inner glass core surrounded by a glass like material which has low refractive index.
Parts of fiber cable
  Core
  Cladding
  Protective coating
It works on the concept of total internal reflection.
  R.I(core) > R.I(cladding)
  Angle of incidence > critical angle

## Slide 40: Fibre Optic Cable

## Slide 41: Types of Fiber Optic Cable
Single node: max length 2 km
Multi node

## Slide 42: Advantages
It is immune to electrical/mechanical interface.
Highly suitable for harsh environment
Secure transmission
Used for broadband transmission.

## Slide 43: Disadvantages
Installation is difficult(glass is very fragile)
Connecting two fibers is difficult.
Connection loss
Most expensive

## Slide 44
Fiber optics: Bending of light ray
Lets understand the fundamental behavior of light to understand the working of fiber optics
Medium Glass
Notes: Refraction: When light pass from one medium to another then it ray of light deviate from path change it is called refraction.
Less dense medium is air and more dense medium is water.
In Dia1 light paases from more dense to less dense then it will deviate when it moves to less dense.
When value of Angle of incidence increase than critical then in 3rd diag gives tiR.
Core refractive index=1.52
Cladding refractive index = 1.48

## Slide 45: Fiber optic cable
Refraction: light passes through a prism. Lights gets bend instead of going straight. This known as refraction. Nair > Nglass

## Slide 46: Fiber optic cable
Refraction is the reason pencil looks bend in the glass of water. This simple technique is used in fiber optic cable.

## Slide 47: Fiber optics: Bending of light ray

## Slide 48: Optical Fiber

## Slide 49: Propagation Modes
Mode
Multi mode
Step index
Graded index
Single mode

## Slide 50: Modes
Multimode, Step Index
Multimode, Graded Index
Singlemode

## Slide 51: Fiber-optic Cable Connectors

## Slide 52: Unguided Media: Wireless
Unguided media transport electromagnetic waves without using a physical conductor. This type of communication is often referred to as wireless communication.
Types of unguided media: -
  Radio Waves
  Microwaves
  Infrared

## Slide 53: Electromagnetic Spectrum for Wireless Communication

## Slide 54: Propagation Methods

## Slide 55: Wireless Transmission Waves
Wireless Transmission
Radio wave
Microwave
Infrared

## Slide 56: Radio Wave
Radio waves are used for multicast communications, such as radio and television, and paging systems. They can penetrate through walls.
Highly regulated. Use omni directional antennas.

## Slide 57: Omnidirectional Antenna

## Slide 58: Advantages of Radio Wave
Inexpensive mode of information exchange.
No land needs to be acquired for laying cables.
Installation and maintenance of devices is cheap.

## Slide 59: Disadvantages of Radio Wave
Insecure communication medium
Prone to weather changes like rain, thunderstorms, etc.

## Slide 60: MicroWave
Microwaves are used for unicast communication such as cellular telephones, satellite networks, and wireless LANs.
Higher frequency ranges cannot penetrate walls.
Use directional antennas - point to point line of sight communications.

## Slide 61: Unidirectional Antennas
Dish Antenna
Horn Antenna

## Slide 62: Drawbacks
They cannot pass through microwave buildings.
Bad weather influences signal transmission.
They are frequency dependent.

## Slide 63: Infrared Signals
Infrared signals can be used for short-range communication in a closed area using line-of-sight propagation.

## Slide 64: Infrared Signals
Infrared signals can be used for short-range communication in a closed area using line-of-sight propagation.
Infrared communication is unreliable outside the building because the sun rays will interfere with the infrared waves.
Infrared waves cannot penetrate the walls.