## Slide 2
After this lecture you will be able to
  learn different types of framing techniques
  differentiate between fixed and variable size framing
  introduction to flow control and error control

## Slide 3: Introduction
Data link control
Media Access control
Two functions of data link layer
1. Deals with communication between two adjacent nodes.
2. Include framing, flow and error control and s/w implemented protocols.
1. How to share the link

## Slide 4: Introduction
Header | Payload Field | Trailer
Header | Payload Field | Trailer
Packet
Packet
Frame
Sending Machine
Receiving Machine

## Slide 5: Parts of a Frame
Flag | Header | Payload Field | Trailer | Flag

## Slide 6: Services Provided By The Data Link Protocols
Framing
Flow Control
Error Detection and/or Correction
Multipoint transmission

## Slide 7: Framing
The data link layer needs to pack bits into frames, so that each frame is distinguishable from another. Our postal system practices a type of framing. The simple act of inserting a letter into an envelope separates one piece of information from another; the envelope serves as the delimiter.

## Slide 8: Framing
Each envelope defines the sender and receiver addresses since the postal system is a many-to-many carrier facility.
Sender Address
Receiver
Address

## Slide 9: Framing
Sender Address
Receiver
Address
Where the packet is to go

## Slide 10: Problems in Framing
Detecting start of the frame
How do station detect a frame
Detecting end of frame

## Slide 11: Framing
Two Types of framing:-
    Fixed sized framing
    Variable sized framing

## Slide 12: Fixed Size Framing
No need for defining the boundaries of the frames.
Size itself can be used as a delimit.
Example
  ATM wide-area network, which uses frames of fixed size called cells

## Slide 13: Drawbacks of Fixed Size Framing
It suffers from internal fragmentation if data size is less than frame size.

## Slide 14: Variable-Size Framing
Need a way to define the end of the frame and the beginning of the next.
This can be done in two ways:-
  Length field
  End Delimiter (ED)

## Slide 15: Variable-Size Framing
End Delimiter problem can be solved in two ways:-
Approaches
A bit-oriented approach/Bit Stuffing
A character-oriented approach/ Byte Stuffing

## Slide 16: Character-Oriented Protocols
Source and destination address
Separate one frame from another
Flag | Header |  |  |  | … |  |  | Trailer | Flag
Data from upper layer
Variable number of characters
Error detection and correction redundant bits (multiples of 8 bit)

## Slide 17: Character-Oriented Protocols/Byte Stuffing
Used when frames consist of character. If data contains ED then, byte is stuffed into data to differentiate it from ED.

## Slide 18: Character-Oriented Protocols/Byte Stuffing
Example
  Let ED = “$”

## Slide 19: Character-Oriented Protocols/Byte Stuffing
Example
  Let End Delimiter = “$” (if data contains ‘$’ anywhere, it can be escaped using ‘\O’ character. )
  if data contains ‘ \0$ ’ then

## Slide 20: Character-Oriented Protocols/Byte Stuffing
Example
  if data contains ‘ \0$ ’ then one more ESC character will be added
  use \0\0\0$ ($ is escaped using \O and \O is escaped using \O)

## Slide 21: Bytestuffing and Unstuffing

## Slide 22: Byte-Stuffing and Unstuffing
When it encounters this pattern in the middle of the data, thinks it has reached the end of the frame.
The data section is stuffed with an extra byte.

## Slide 23: Byte-Stuffing and Unstuffing
Escape characters that are part of the text must also be marked by another escape character
In other words, if the escape character is part of the text, an extra one is added to show that the second one is part of the text.

## Slide 24: Byte-Stuffing and Unstuffing at Receiving Side

## Slide 25: Byte-Stuffing and Unstuffing at Receiving Side
Remove ESC character so that next flag to be treated as a data not as a delemiter.
Remove ESC character so that next ESC to be treated as a data not as a delimiter.

## Slide 26: Problem in Character Oriented Protocol
The universal coding systems in use today, such as Unicode, have 16-bit and 32-bit characters that conflict with 8-bit characters.
We can say that in general, the tendency is moving toward the bit-oriented protocols.
It is very costly and obsolete method.

## Slide 27: Bit-Oriented Protocols
The data section of a frame is a sequence of bits to be interpreted by the upper layer as text, graphic, audio, video, and so on.
However, in addition to headers (and possible trailers), we still need a delimiter to separate one frame from the other.

## Slide 28: Bit Oriented Protocol
Example:
  Let ED = 01111 and if data = 01111.
  Sender stuffs a bit to break the pattern i.e. here appends a 0 in data = 011101.
  Receiver receives the frame. –> If data contains 011101, receiver removes the 0 and reads the data

## Slide 29: Bit Oriented Protocol
Example:
  Let ED = 01111 and if data = 01111.
  Sender stuffs a bit to break the pattern i.e. here appends a 0 in data = 011101.
  Receiver receives the frame. –> If data contains 011101, receiver removes the 0 and reads the data

## Slide 30: Bit Oriented Protocol
Example:
  Let ED = 01111 and if data = 01111.
  Sender stuffs a bit to break the pattern i.e. here appends a 0 in data = 011101.
  Receiver receives the frame. –> If data contains 011101, receiver removes the 0 and reads the data

## Slide 31: Bit Oriented Protocol
A frame in a bit-oriented protocol. Most protocols use a special 8-bit pattern flag 01111110 as the delimiter to define the beginning and the end of the frame.
01111110 | Header | 01111010110 … 11011110 | Trailer | 01111110
Data from upper layer
Variable number of bits
Flag
Flag

## Slide 32: Bit Oriented Protocol
Note that even if we have a 0 after five 1s, we still stuff a O. The 0 will be removed by the receiver.
Bit Stuffing
0 1 1 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 0
0 1 1 0 1 1 1 1 1 0 1 1 1 1 1 0 1 1 1 1 1 0 1 0 0 1 0
0 1 1 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 0
Stuffed Bits

## Slide 33: Flow Control
Flow Control
  It is an important function of the Data Link Layer. It refers to a set of procedures that tells the sender how much data it can transmit before waiting for acknowledgement from the receiver.

## Slide 34: Error Control
Error Control
  The error control function of data link layer detects the errors in transmitted frames and re-transmit all the erroneous frames.