## Slide 2
After this lecture, you will be able to
  Recall link layer services.
  Understand flow control.
  Understand all techniques for noiseless channels.

## Slide 3: Introduction
Throw
Catch

## Slide 4: Introduction
Buffer
Throw
Catch

## Slide 5: Types of Data Link Protocols
Basic Functions in the Datalink Layer
Framing
Error control
Flow control

## Slide 6: Types of Data Link Protocols
Basic Functions in the Datalink Layer
Framing
Error control
Flow control

## Slide 7: Types of Data Link Protocols
Basic Functions in the Datalink Layer
Framing
Error control
Flow control

## Slide 8: Types of Data Link Protocols
Basic Functions in the Datalink Layer
Framing
Error control
Flow control

## Slide 9: Types of Data Link Protocols
Data Link Protocols
For Noiseless Channels
For Noisy Channels
Simplex
Stop and wait
Stop and Wait ARQ
Go- back-N ARQ
Selective Repeat ARQ

## Slide 10: Noiseless Channels
An ideal channel in which no frames are lost, duplicated or corrupted is regarded as Noiseless Channel.
It provides flow-control mechanism but does not provide any error control mechanism.

## Slide 11: Difference Between Protocols
Unidirectional | Bidirectional
Data frames travel from one node, called the sender, to another node, called the receiver | Data flow in both directions
Less Complex | Bidirectional protocols are more complex

## Slide 12: Simplex Protocol
No flow or error control
Unidirectional protocol.
Receiver can immediately handle any frame it receives.
No sequence number or acknowledgements are used here.

## Slide 13: Simplest Protocol

## Slide 14: Simplest Protocol
Design of the simplest protocol with no flow control and error control

## Slide 15: Simplest Protocol (Sender Aide Algorithm)
while(true) | //repeat forever
{ | 
WaitForEvent(); | //Sleep until an event occurs
if(Event(RequestToSend) | //There is a packet to send
{ | 
GetData(); | //takes a data packet from the network layer
MakeFrame(); | //adds a header and delimiter flags to the data packet to make a frame
SendFrame(); | //delivers the frame to the physical layer for transmission.
} } | 

## Slide 16: Simplest Protocol (Receiver Side Algorithm)
while(true) | //repeat forever
{ | 
WaitForEvent(); | //Sleep until an event occurs
if(Event(Arrivalnotification) | //There is a packet to send
{ | 
ReceiveFrame(); | //receives the frame from the physical layer
ExtractData(); | //extracts the data from the frame
Deliverdata(); | //delivers the data to the network layer.
} } | 

## Slide 17: STOP and WAIT Protocol

## Slide 18: Stop-and-Wait Protocol
Sender
Receiver
Data
Data
Data
Ack
Ack
Ack
After Consumption
Flow Control

## Slide 19: Stop and Wait protocol
0 | 1 | 0 | 1 | 0
Sn next Frame to send
0 | 1 | 0 | 1 | 0
Rn next Frame to receive

## Slide 20: Stop and Wait protocol
\ |  | 
Seq No
Dataframe
\ |  | 
ackNo
ACK frame

## Slide 21: Stop and Wait Protocol (Sender Side Algorithm)
while(true) | //repeat forever
canSend=true | //Allow the first frame to go
{ | 
WaitForEvent(); | //Sleep until an event occurs
if(Event(RequestToSend) And canSend | //There is a packet to send
{ | 
GetData(); | //takes a data packet from the network layer
MakeFrame(); | //adds a header and delimiter flags to the data packet to make a frame
SendFrame(); | //delivers the frame to the physical layer for transmission.
canSend=false; } | //cannot send until ack arrives

## Slide 22: Stop and Wait Protocol (Sender Side Algorithm)
WaitForEvent() | //Sleep until an event occurs
If(Event(Arrival Notification) { | //An ACK has arrived
ReceiveFrame(); canSend=true; }} | //Receive ACK frame

## Slide 23: Stop and Wait Protocol (Receiver Side Algorithm)
while(true) | //repeat forever
{ WaitForEvent(); | //Sleep until an Event occurs
If(Event(Arrival Notification) { | //An ACK has arrived
ReceiveFrame(); | 
ExtractData(); | 
Deliverdata(); | //Deliver data to network layer
SendFrame(); | //Send an ACK Frame
}} | 

## Slide 24: Problem with Stop and Wait - Lost Data
Sender
Receiver
Data
Sender waits for Ack Receiver waits for data
For infinite amount of time
X

## Slide 25: Problem with Stop and Wait – Lost Acknowledgment
Sender
Receiver
Data
Sender waits for Ack For infinite amount of time
X

## Slide 26: Problem Due to Delayed Data or Acknowledgment
Sender
Receiver
Data