## Slide 2
After this lecture you will be able to
  understand the working of simple stop and wait ARQ protocol.
  understand the problem with stop and wait protocol
  understand the working of Go-back-N ARQ

## Slide 3: Data Link Protocols
Data Link Protocol
For Noiseless Channels
Simplex
Stop & Wait
For Noisy Channels
Stop & Wait ARQ
Go-back-N ARQ
Selective Repeat ARQ
Sliding Window Protocol

## Slide 4: Stop-and-Wait Automatic Repeat Request
Three problems are resolved by Stop and Wait ARQ (Automatic Repeat Request) that does both error control and flow control.
Lost data
Lost Ack
Delay Ack
Stop and wait ARQ = Stop and wait + TimeOut + Seqno(data) + Seqno(Ack)

## Slide 5: Stop and Wait ARQ Protocol
Idea of stop and wait protocol is straightforward.
After transmitting one frame, the sender waits for an acknowledgement before transmitting the next frame.
If acknowledgment does not arrive after a certain period of time, the sender times out and retransmit the original frame.

## Slide 6: Stop and Wait ARQ Protocol
Idea of stop and wait protocol is straightforward.
After transmitting one frame, the sender waits for an acknowledgement before transmitting the next frame.
If acknowledgment does not arrive after a certain period of time, the sender times out and retransmit the original frame.

## Slide 7: Stop and Wait ARQ Protocol
Idea of stop and wait protocol is straightforward.
After transmitting one frame, the sender waits for an acknowledgement before transmitting the next frame.
If acknowledgment does not arrive after a certain period of time, the sender times out and retransmit the original frame.

## Slide 8: Stop and Wait ARQ Protocol
Sender

## Slide 9: Stop and Wait ARQ Protocol
Sender
Receiver

## Slide 10: Stop and Wait ARQ Protocol
Sender
Receiver
SCENARIO 1
Data packet

## Slide 11: Stop and Wait ARQ Protocol
Sender
Receiver
Acknowledgment
The ACK is received before the timer expires.
SCENARIO 1
Timer Time
Out
Data packet

## Slide 12: Stop and Wait ARQ Protocol
Sender
Receiver
The original frame is lost
SCENARIO 2
Timer Time
Out
Timer Time
Out
Timer Time
Out
Acknowledgment
Data packet
Data packet
Data packet
Acknowledgment

## Slide 13: Stop and Wait ARQ Protocol
Sender
Receiver
The acknowledgment is lost
SCENARIO 3
Timer Time
Out
Timer Time
Out
Data packet
Data packet
ACK
ACK

## Slide 14: Stop and Wait ARQ Protocol
Sender
Receiver
Time out fires too soon. Before getting ack, the timer expires. ACK has reached the sender lately. Ack got after timer expires. It will resent the frame after ack not reached.
SCENARIO 4
Timer Time
Out
Timer Time
Out
Duplicate frame
Frame
ACK
Frame
ACK

## Slide 15: Stop-and-Wait Automatic Repeat Request
Delayed Acknowledgement
  After timeout on sender side, a long delayed acknowledgement might be wrongly considered as acknowledgement of some other recent packet.
  This is resolved by introducing sequence number for acknowledgement also

## Slide 16: Drawbacks
One Frame at a time
Poor utilization of bandwidth
Poor performance (if bandwidth not utilized properly, obviously poor performance)

## Slide 17: Issue with Stop and Wait ARQ
Big performance issues as sender always waits for acknowledgement even if it has next packet ready to send.
Consider a situation where you have a high bandwidth connection and propagation delay is also high. To solve this problem, we can send more than one packet at a time with a larger sequence numbers

## Slide 18: Issue with Stop and Wait ARQ
Big performance issues as sender always waits for acknowledgement even if it has next packet ready to send.
Consider a situation where you have a high bandwidth connection and propagation delay is also high. To solve this problem, we can send more than one packet at a time with a larger sequence numbers

## Slide 19: Important Stop and Wait ARQ
Stop and Wait ARQ may work fine where propagation delay is very less for example LAN connections.
Performs badly for distant connections like satellite connection.

## Slide 20: Sliding Window Protocol
Is actually a theoretical concept in which we have only talked about what should be the sender window size (1+2a) in order to increase the efficiency of stop and wait arq.
Practically it is implemented in two protocols namely :
  Go Back N (GBN)
  Selective Repeat (SR)

## Slide 21: Sliding Window Protocol
Is actually a theoretical concept in which we have only talked about what should be the sender window size (1+2a) in order to increase the efficiency of stop and wait arq.
Practically it is implemented in two protocols namely :
  Go Back N (GBN)
  Selective Repeat (SR)

## Slide 22: Stop and Wait vs Sliding Window Protocol
Stop and wait Protocol | Sliding window protocol
Only one frame is sent at a time. Sender will not send the next frame before receiving the ack. | Multiple frames can be sent at a time. The variations in sliding window protocol is Go-Back-N ARQ, Selective repeat ARQ

## Slide 23: Go-Back-N ARQ
Go-Back-N ARQ
N is the sender window size

## Slide 24: Go-Back-N
It uses the concept of protocol pipelining i.e. the sender can send multiple frames before receiving the acknowledgment from the first frame.
There are finite number of frames and the frames are numbered in a sequential manner.(number of frames can be sent so We need to distinguish one frame from another frame).
The number of frames that can be sent depend upon the window size of the sender.
All frames in the current window are transmitted.

## Slide 25: Go-Back-N
It uses the concept of protocol pipelining i.e. the sender can send multiple frames before receiving the acknowledgment from the first frame.
There are finite number of frames and the frames are numbered in a sequential manner.(number of frames can be sent so We need to distinguish one frame from another frame).
The number of frames that can be sent depend upon the window size of the sender.
All frames in the current window are transmitted.

## Slide 26: Go-Back-N
It uses the concept of protocol pipelining i.e. the sender can send multiple frames before receiving the acknowledgment from the first frame.
There are finite number of frames and the frames are numbered in a sequential manner.(number of frames can be sent so We need to distinguish one frame from another frame).
The number of frames that can be sent depend upon the window size of the sender.
All frames in the current window are transmitted.

## Slide 27: Go-Back-N
It uses the concept of protocol pipelining i.e. the sender can send multiple frames before receiving the acknowledgment from the first frame.
There are finite number of frames and the frames are numbered in a sequential manner.(number of frames can be sent so We need to distinguish one frame from another frame).
The number of frames that can be sent depend upon the window size of the sender.
All frames in the current window are transmitted.

## Slide 28: Go Back N (GBN) Protocol
The three main characteristic features of GBN are:
  Sender Window Size (WS)
  Receiver Window Size (WR)
  Acknowledgements

## Slide 29: Go-Back-N
The size of the sending window determines the sequence number of the outbound frames.

## Slide 30: Go-Back-N
N-Sender window size
For example, if sending window size is 4(22) , then the sequence number size will be 0,1,2,3,0,1,2,3,0,1,2,3,0,1…and so on.
The number of bits in the sequence number is 2 to generate the binary sequence 00,01,10,11.
00  0
01  1
10  2
11  3

## Slide 31: Go-Back-N ARQ
Sender

## Slide 32: Go-Back-N ARQ
Sender
Receiver

## Slide 33: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 34: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Window Size is 4

## Slide 35: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0
Window Size is 4

## Slide 36: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0
1
Window Size is 4

## Slide 37: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0
1
2
Window Size is 4

## Slide 38: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0
1
2
3
Window Size is 4

## Slide 39: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0
1
2
3
0
Sliding Window
4
Window Size is 4

## Slide 40: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0
1
2
3
0
Sliding Window
4
Window Size is 4

## Slide 41: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0
1
2
3
0
Sliding Window
4
5
Window Size is 4

## Slide 42: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0
1
2
3
0
Sliding Window
4
5
1
2
ACK not received in time. So, sender times out.
Window Size is 4

## Slide 43: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0
1
2
3
0
Sliding Window
4
5
1
2
Window Size is 4
ACK not received in time. So, sender times out.

## Slide 44: Go-Back-N ARQ
Sender
Receiver
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Frame 2,3,4 and 5 will be retransmit
0
1
2
3
0
Sliding Window
4
5
1
2
2
3
4
5
Discarded
Window Size is 4

## Slide 45: Acknowledgements
Cumulative Ack: One acknowledgement is used for many packets. The main advantage is traffic is less. A disadvantage is less reliability as if one ack is the loss that would mean that all the packets sent are lost.
Independent Ack: If every packet is going to get acknowledgement independently. Reliability is high here but a disadvantage is that traffic is also high since for every packet we are receiving independent ack.

## Slide 46: Two Types of Acknowledgement
Cummulative
Independent
1
2
3
2
3
4
4
3
2
1
ACK - 5