## Slide 2
After this lecture, student will be able to
  understand bit-oriented protocol.
  know the frame format and types of HDLC frame.
  know the byte oriented protocol.
  understand the frame format of PPP.
  understand the byte stuffing in PPP Frame.

## Slide 3: Bit Oriented Approach
It simply views the frame as a collection of bits.
Bit Oriented protocol is HDLC

## Slide 4: HDLC
High Level Data Link Control(HDLC) basically provides reliable delivery of data frames over a network or communication link.
HDLC provides various operations such as
  framing, data transparency, error detection, and correction, and even flow control

## Slide 5: HDLC
The Synchronous Data link control(SDLC) protocol developed by IBM is an example of bit-oriented protocol.
SDLC was standardized by the ISO as the High-level data link control (HDLC) protocol.
Bit-Oriented Protocol.
Point to Point and Multipoint Communications.

## Slide 6: Transfer Modes of HDLC

## Slide 7: HDLC-Frame Format
8
Beginning Sequence

## Slide 8: HDLC-Frame Format
16
Header

## Slide 9: HDLC-Frame Format
Body

## Slide 10: HDLC-Frame Format
16
CRC

## Slide 11: HDLC-Frame Format
8
Ending Sequence

## Slide 12: HDLC-Frame Format
8 | 16 |  | 16 | 8
Beginning Sequence | Header | Body | CRC | Ending Sequence

## Slide 13: HDLC-Frame Format
8 | 16 |  | 16 | 8
Beginning Sequence | Header | Body | CRC | Ending Sequence
Beginning and Ending Sequences: 01111110
This sequence is also transmitted during any times that the link is idle so that the sender and receiver can keep their clocks synchronized.
Header: Address and control field.
Body: Payload?(Variable Size)
CRC-Cyclic Redundancy Check-Error Detection.

## Slide 14: Types of HDLC Frames
Types of Frame
I-frame : Information Frame.
S-Frame: Supervisory Frame
U-Frame: Un-numbered Frame
The type of frame is determined by the control

## Slide 15: Types of HDLC Frames
I-Frame | 1st bit is 0
S-Frame | 1st two bits is 10
U-Frame | 1st two bits is 11

## Slide 16
PPP(point-to-point) Protocol

## Slide 17: Byte Oriented Protocol
It simply views the frame as a collection of bytes or characters.
Basically, we have 3 protocols
BISYNC <-> Binary Synchronous Communication Protocol.
PPP <-> Point-to-Point Protocol.
DDCMP <-> Digital Data Communication Message Protocol.

## Slide 18: PPP
Data link layer protocol.
PPP is a WAN protocol and which is commonly run over internet.
It is widely used in broadband communications having heavy loads and high speeds.
It is also used to transmit multiprotocol data between two directly connected ?(point-to-point) computers.

## Slide 19: Components of PPP
Encapsulation Component
Link Control Protocol (LCP)
Authentication Protocols (AP)
Network Control Protocols (NCPs)
NCP
IPCP
OSINLCP
…………
IPXCP
AP
PAP
CHAP
LCP
Control Protocols

## Slide 20: PPP-Frame Format

## Slide 21: Byte Stuffing in PPP Frame
Byte stuffing is used is PPP payload field whenever the flag sequence appears in the message, so that the receiver does not consider it as the end of the frame. The escape byte, 01111101, is stuffed before every byte that contains the same byte as the flag byte or the escape byte. The receiver on receiving the message removes the escape byte before passing it onto the network layer.