## Slide 2
After this lecture, student will be able to
  understand CSMA protocol
  analyze types of CSMA
  understand the behavior of three persistent methods

## Slide 3: CSMA
Carrier Sense multiple access.
To minimize the chance of collision and, therfore, increase the performance, the CSMA method was developed.
Principal of CSMA: “sense before transmit” or “listen before talk”.

## Slide 4: Example
A
B
C
D
E
F

## Slide 5: Example
A
B
C
D
E
F

## Slide 6: CSMA
What about carrier?
Carrier busy = Transmission is taking place.(if station wants to send data,
Carrier idle = No transmission currently take place.
The possibility of collision still exists because of propagation delay: a station may sense the medium and find it idle, only because the first bit sent by another station has not yet been received.

## Slide 7: CSMA
What about carrier?
Carrier busy = Transmission is taking place.(if station wants to send data,
Carrier idle = No transmission currently take place.
The possibility of collision still exists because of propagation delay: a station may sense the medium and find it idle, only because the first bit sent by another station has not yet been received.

## Slide 8: CSMA
What about carrier?
Carrier busy = Transmission is taking place.(if station wants to send data,
Carrier idle = No transmission currently take place.
The possibility of collision still exists because of propagation delay: a station may sense the medium and find it idle, only because the first bit sent by another station has not yet been received.

## Slide 9: CSMA
What about carrier?
Carrier busy = Transmission is taking place.(if station wants to send data,
Carrier idle = No transmission currently take place.
The possibility of collision still exists because of propagation delay: a station may sense the medium and find it idle, only because the first bit sent by another station has not yet been received.

## Slide 10: Example
Frame
A
B
C
D
E
F

## Slide 11: Example
Frame
A
B
C
D
E
F

## Slide 12: CSMA
The possibility of collision still exists because of propagation delay: a station may sense the medium and find it idle, only because the first bit sent by another station has not yet been received.

## Slide 13: CSMA
Vulnerable Time

## Slide 14: Types of CSMA
1-Persistent CSMA
P-Persistent CSMA
Non-Persistent CSMA
O-Persistent CSMA

## Slide 15: Types of CSMA
Modified Protocols are:-
  CSMA/CD(CSMA with collision detection)
  CSMA/CA(CSMA with collision avoidance)

## Slide 16: 1-persistent CSMA
Before sending the data, the station first listens to the channel to see if anyone else is transmitting the data at that moment.
If channel is idle, the station transmits a frame.
If channel is busy, then it senses the transmission medium continuously until it becomes idle.

## Slide 17: 1-persistent CSMA
Before sending the data, the station first listens to the channel to see if anyone else is transmitting the data at that moment.
If channel is idle, the station transmits a frame.
If channel is busy, then it senses the transmission medium continuously until it becomes idle.

## Slide 18: 1-persistent CSMA
Before sending the data, the station first listens to the channel to see if anyone else is transmitting the data at that moment.
If channel is idle, the station transmits a frame.
If channel is busy, then it senses the transmission medium continuously until it becomes idle.

## Slide 19: 1-Persistent CSMA
Ques:- Why it is called 1-Persistent CSMA?

## Slide 20: 1-Persistent CSMA
Ques:- Why it is called 1-Persistent CSMA?
Ans:- Since the station transmits a frame with the probability of 1 when the carrier or channel is idle, this scheme of CSMA is called as 1-persistent CSMA.
The propagation delay has an important effect on the performance of the protocol.

## Slide 21: 1-Persistent CSMA
Question:- Why propagation delay is important?

## Slide 22: 1-Persistent CSMA
Question:- Why propagation delay is important?
Ans:- The longer the propagation delay, the more important this effect becomes , and the worse the performance of the protocol

## Slide 23: Example
Shared medium/propagation medium
Frame
A
B
C
D
E
F

## Slide 24: Example
Shared medium/propagation medium
Frame
A
B
C
D
E
F
Frame

## Slide 25: Example
Shared medium/propagation medium
Frame
A
B
C
D
E
F
Frame
Collision

## Slide 26: Non-Persistent CSMA
Before sending, a station senses the channel.
If no one else is sending, the station begin doing so itself.
1-Persistent CSMA | Non-Persistent CSMA
Continuously Sense | Does not continuously sense

## Slide 27: Non-Persistent CSMA
Ques:- What happens if it does not continuously sense?

## Slide 28: Non-Persistent CSMA
Ques:- What happens if it does not continuously sense?
Ans:- The previous transmission might have already been completed ,the channel is still free , this might have not noticed by the station that the channel is free because it is randomly checking.

## Slide 29
It waits random period of time and then repeats the algorithm.
Consequently, this algorithm leads to better channel utilization but longer delays than 1-persistent CSMA.

## Slide 30: P-Persistent CSMA
It applies on slotted channel.

## Slide 31: P-Persistent CSMA
When station becomes ready to send, it senses the channel.

## Slide 32: P-Persistent CSMA
With probability Q=1-P, it defers the next slot.

## Slide 33: P-Persistent CSMA
If that slot is also idle, it either transmits or defers again, with probabilities P and Q.

## Slide 34: P-Persistent CSMA
This process is repeated until either the frame has been transmitted or another station has begun transmitting.

## Slide 35: P-Persistent CSMA
In the latter case, the unlucky station acts as if there had been a collision.

## Slide 36: P-Persistent CSMA
This process is repeated until either the frame has been transmitted or another station has begun transmitting.

## Slide 37: Behavior of 1 - Persistent Methods
Behavior Of 1 Persistent Methods
Continuously Sense
Sense & Transmit
Time
Busy

## Slide 38: Behavior Of Non-Persistent Methods
Behavior Of Non - Persistent Methods
Sense
Sense & Transmit
Time
Busy
Sense
Wait
Wait

## Slide 39: CSMA
Behavior of P Persistent Methods
Continuously Sense
Sense & Transmit
Time
Busy
Transmit
Time Slot
Time Slot
Time Slot

## Slide 40: O-Persistent CSMA
Each node is assigned a transmission order by a supervisory node.