## Slide 2
After this lecture you will be able to
  understand Classful Addressing and classless addressing

## Slide 3: Classful Addressing
IPv4 addressing, at its inception, used the concept of classes. This architecture is called classful addressing.

## Slide 4: Classful Addressing
IPv4 addressing, at its inception, used the concept of classes. This architecture is called classful addressing.
Class A
Class B
Class C
Class D
Class E

## Slide 5: Classful Addressing
There are two prevalent notations to show an IPv4 address:
Class A
Class B
Class C
Class D
Class E
Binary Notation
Dotted Decimal Notation

## Slide 6: Binary Notation
In binary notation, the IPv4 address is displayed as 32 bits.
Each octet is often referred to as a byte.
So it is common to hear an IPv4 address referred to as a 32-bit address or a 4-byte address.
The following is an example of an IPv4 address in binary notation:
01110101 10010101 00011101 00000010

## Slide 7: Decimal Notation
To make the IPv4 address more compact and easier to read, Internet addresses are usually written in decimal form with a decimal point (dot) separating the bytes.
For example:
117.149.29.2

## Slide 8: Dotted-decimal Notation and Binary Notation
10000000
000010II
00000011
00011111
128.11.3.31
Dotted-decimal notation and binary notation for an IPv4 address

## Slide 9: Important points to remember
There must be no leading zero (045).

## Slide 10: Important points to remember
There must be no leading zero (045).
There can be no more than four numbers in an IPv4 address.
N.N.N.N.N

## Slide 11: Important points to remember
There must be no leading zero (045).
There can be no more than four numbers in an IPv4 address.
Each number needs to be less than or equal to 255 (301 is outside this range).
255.272.255.255

## Slide 12: Important points to remember
A mixture of binary notation and dotted-decimal notation is not allowed
172. 00101000. 254. 11001100

## Slide 13: Find the error, if any, in the following IPv4 addresses
a. 111.56.045.78
b. 221.34.7.8.20
c. 75.45.301.14
d. 11100010.23.14.67

## Slide 14: Find the error, if any, in the following IPv4 addresses
a. 111.56.045.78
b. 221.34.7.8.20
c. 75.45.301.14
d. 11100010.23.14.67 //mix of binary and dotted decimal notation.

## Slide 15: Classful Addressing
N |  |  | 
Class A
Class B
Class C
Class D
Class E
Binary Notation
NN |  |  | 
NNN |  |  | 
NNNN |  |  | 
NNNN |  |  | 
Class of the address

## Slide 16: Classful Addressing
0 |  |  | 
Class A
Class B
Class C
Class D
Class E
Binary Notation
10 |  |  | 
110 |  |  | 
1111 |  |  | 
1110 |  |  | 
Class of the address

## Slide 17: Example Binary Notation
Find the class of each address.
00000001 | 00001011 | 00001011 | 11101111

## Slide 18: Example Binary Notation
Find the class of each address.
00000001 | 00001011 | 00001011 | 11101111
First Bit is 0, it belongs to Class A

## Slide 19: Example Binary Notation
Find the class of each address.
11000001 | 10000011 | 00011011 | 11101111

## Slide 20: Example Binary Notation
Find the class of each address.
11000001 | 10000011 | 00011011 | 11101111
The first 2 bits are 1; the third bit is O. This is a class C address.

## Slide 21: Classful Addressing
0 - 127 |  |  | 
Class A
Class B
Class C
Class D
Class E
Dotted Decimal Notation
128-191 |  |  | 
192-223 |  |  | 
240-255 |  |  | 
224-239 |  |  | 
Class of the address

## Slide 22: Example Dotted Decimal Notation
Find the class of each address ?
14.23.120.8 - ?
252.5.15.111 - ?

## Slide 23: Example Dotted Decimal Notation
Find the class of each address ?
14.23.120.8 - ?
252.5.15.111 - ?
Between 0 and 127. the class is A.
Between 240 and 255 . the class is E.

## Slide 24: Division of Classes
Classes are divided into
NetID
HostID

## Slide 25: NetID and HostID
In classful addressing, an IP address in class A, B, or C is divided into netid and hostid.
These parts are of varying lengths, depending on the class of the address.
Note that the concept does not apply to classes D and E.

## Slide 26: NETID and HOSTID
In Class A
NetID | HostID | HostID | HostID

## Slide 27: Class A IP address
IP address begin with 0
7 remaining bits in network part
  Only 128 possible class A network.
24 bits in local part
  Over 16 million hosts per class A network.
All class A network parts are assigned or reserved.

## Slide 28: Class A IP Address
NetID | HostID | HostID | HostID
0
8
7
31
Binary Notation

## Slide 29: Class A IP Address
NetID | HostID | HostID | HostID
0
8
7
31

## Slide 30: Class A IP Address
0.0.0.0 to 0.255.255.255
127.0.0.0 to 127.255.255.255
We never assigned these to any hosts…these representing default network.
0 – default network
127---Loopback address…check whether NIC is working properly or not
NetID | HostID | HostID | HostID
0
8
7
31

## Slide 31: Summary of Class A IP address
Class | Leading Bits | Size of network number field | Size of rest bit field | Number of networks | Address per network
Class A | 0 | 8 | 24 | 128(2pow 7) | 16,777,216 (2pow24)
0.0.0.0 to 127.255.255.255
But in actual we can use
1.0.0.0 to 126.255.255.255
Range Starts from

## Slide 32: NETID and HOSTID
In Class B
NetID | NetID | HostID | HostID

## Slide 33: Class B IP address
16 bits for network part 16 bits for host part
A balance between number of networks and hosts.
IP address begins with 10(1st zero in second position)
14 remaining bits in network part
  Over 16,000 possible class B network
16 bits in local part
  Over 65,000 possible hosts

## Slide 34: Class B
10nnnnnn.nnnnnnnn.hhhhhhhh.hhhhhhhh
Range from
10000000.00000000.00000000.00000000 to
10111111.11111111.11111111.11111111
NETID(starting with 10) | Host ID
16 bits
16 bits
32 bits
Binary Notation

## Slide 35: Class B
Range from
10000000.00000000.00000000.00000000
To
10111111.11111111.11111111.11111111
Decimal conversion
128.0.0.0 to 191.255.255.255
Decimal Notation

## Slide 36: Class B
Exceptions in Class B IP Address
  169.254.x.x
We never assigned this IP address to any host because this range reserve for APIPA.
  169.254.x.x is a private IP Addressing space reserved by Microsoft which it assigns automatically to your Network Adapter if it cannot get an IP Address from the DHCP Server

## Slide 37: Summary of Class B IP address
Class | Leading Bits | Size of network number bit field | Size of text bit field | Number of networks | Address per network
B | 10 | 16 | 16 | 16384(2 pow 14) | 65536(2 pow 16)
128.0.0.0 to 191.255.255.255

## Slide 38: NETID and HOSTID
In Class C
NetID | NetID | NetID | HostID

## Slide 39: Class C
24 bits for network address and 8 bits for host
Popular and commonly used
IP address begins with 110(1st zero in 3d position)
21 more bits in network part
  Over 2 million possible class C networks
8 bits in local part
  Only 256 possible hosts per class C network.

## Slide 40: Class C
110nnnnn.nnnnnnnn.nnnnnnnn.hhhhhhhh
Range from
11000000.00000000.000000000.00000000
To
11011111.11111111.111111111.11111111
NetID | NetID | NetID | HostID
24 bits
8 bits
0
23
24
31
Binary Notation

## Slide 41: Class C
110nnnnn.nnnnnnnn.nnnnnnnn.hhhhhhhh
Range from
192.0.0.0 to 223.255.255.255
Decimal Notation
NetID | NetID | NetID | HostID
24 bits
8 bits
0
23
24
31

## Slide 42: Summary of Class C
221 because 110 reserve out of 24 network bits
Class | Leading Bits | Size of network number bit field | Size of text bit field | Number of networks | Address per network
C | 110 | 24 | 8 | 2097152(2 pow 21) | 256(2 pow 8)

## Slide 43: Class D IP address
Starts from 224.0.0.0 to 239.255.255.255
Used for multicasting(one to many type)
IP address begins with 1110
Used for multicasting, not defining networks
  Sending message to group of hosts
  Not just to one
  Do not define network or host bits
  Different from broadcasting
  Used for videoconferencing.
1110 | Multicast(28 bit)

## Slide 44: Class D
In binary
11100000.00000000.00000000.00000000
To
11101111.11111111.11111111.11111111
Decimal range
224.0.0.0 to 239.255.255.255

## Slide 45: Popular Class D IP Addresses
224.0.0.0: Base address reserved
224.0.0.1: Used for all multicasting host groups
224.0.0.2: Used for all subnet routers
224.0.0.5 and 224.0.0.6: Used by Open Shortest Path First, an interior gateway protocol for all network segment routing information

## Slide 46: Popular Class D IP Addresses
224.0.0.7 | ST, Internet Stream Protocol (routers)
224.0.0.8 | ST, Internet Stream Protocol (hosts)
224.0.0.9 | RIP, Routing information Protocol version 2
224.0.0.10 | EIGRP, Enhanced IGR. IGRP, Interior Gateway Routing Protocol
224.0.0.11 | Mobile-Agents
224.0.0.12 | DHCP server/relay agent
224.0.0.13 | PIM, Protocol Independent Muticast
224.0.0.14 | RSVP-ENCAPSUATION
224.0.0.15 | CBT, Core Based Trees
224.0.0.16 | Designated-sbm
224.0.0.17 | All-sbm
224.0.0.18 | VRRP, Virtual Redundancy Protocol

## Slide 47: Class E IP Addresses
Class E IP addresses starts from 240.0.0.0. to 255.255.255.255
Reserved for experimental purposes.
IP address begins with 1111.
In Binary Form
11110000.00000000.00000000.00000000
To
11111111.11111111.11111111.11111111
In decimal form
240.0.0.0
To
255.255.255.255
11110 | Future use (27 bit)

## Slide 48: Issues with Classful Addressing
Each class is divided into a fixed number of blocks with each block having a fixed size

## Slide 49: Design of Classful Addressing
Class A addresses were designed for large organizations with a large number of attached hosts or routers.

## Slide 50: Design of Classful Addressing
Class A addresses were designed for large organizations with a large number of attached hosts or routers.
Class B addresses were designed for midsize organizations with tens of thousands of attached hosts or routers.

## Slide 51: Design of Classful Addressing
Class A addresses were designed for large organizations with a large number of attached hosts or routers.
Class B addresses were designed for midsize organizations with tens of thousands of attached hosts or routers.
Class C addresses were designed for small organizations with a small number of attached hosts or routers

## Slide 52
CAN WE SEE FLAW IN THIS DESIGN?

## Slide 53: 1st Flaw in this Design
A block in class A address is too large for almost any organization.
This means most of the addresses in class A were wasted and were not used

## Slide 54: 2nd Flaw in this Design
A block in class B is also very large, probably too large for many of the organizations that received a class B block

## Slide 55: 3rd Flaw in this Design
A block in class C is probably too small for many organizations

## Slide 56: 4rth Flaw in this Design
Class D addresses were designed for multicasting

## Slide 57: Flaws in this Design
Lots of addresses are wasted.
Each address in this class is used to define one group of hosts on the Internet.
The Internet authorities wrongly predicted a need for 268,435,456 groups.
This never happened and many addresses were wasted here too.
And lastly, the Class E addresses were reserved for future use; only a few were used, resulting in another waste of addresses

## Slide 58: Demerit of Classful Addressing
Lack of Internal Address Flexibility
Inefficient Use of Address Space

## Slide 59
Classful addressing, which is almost obsolete, is replaced with classless addressing

## Slide 60: Classless Addressing
To overcome address depletion and give more organizations access to the Internet,

## Slide 61: Classless Addressing
To overcome address depletion and give more organizations access to the Internet,
Classless addressing was designed and implemented. In this scheme, there are no classes, but the addresses are still granted in blocks.

## Slide 62: CIDR
CIDR or Class Inter-Domain Routing was introduced in 1993 to replace classful addressing.
It allows the user to use VLSM or Variable Length Subnet Masks.
No classes.
Only using concept of blocks.
Handled by IANA.
BlockID | Host ID
32 bits

## Slide 63: CIDR NOTATION
/n – representing network ID part.
/n – representing mask( continous 1’s)
/n – representing block
x. y. z. w /n

## Slide 64: CIDR NOTATION
In CIDR subnet masks are denoted by /X.
For example
a subnet of 255.255.255.0 would be denoted by /24.

## Slide 65: CIDR NOTATION
In CIDR subnet masks are denoted by /X.
For example
a subnet of 255.255.255.0 would be denoted by /24.

## Slide 66: CIDR NOTATION
Ques:- How a subnet of 255.255.255.0 would be denoted by /24 ?
Ans:-
First Octet:
11111111
255. 255. 255. 0

## Slide 67: CIDR NOTATION
Ques:- How a subnet of 255.255.255.0 would be denoted by /24 ?
Ans:-
First Octet:
11111111
255. 255. 255. 0
11111111
Second Octet:

## Slide 68: CIDR NOTATION
Ques:- How a subnet of 255.255.255.0 would be denoted by /24 ?
Ans:-
First Octet:
11111111
255. 255. 255. 0
11111111
Second Octet:
11111111
Third Octet

## Slide 69: CIDR NOTATION
Ques:- How a subnet of 255.255.255.0 would be denoted by /24 ?
Ans:-
First Octet:
11111111
255. 255. 255. 0
11111111
Second Octet:
11111111
Third Octet
00000000
Fourth Octet

## Slide 70: CIDR NOTATION
Ques:- How a subnet of 255.255.255.0 would be denoted by /24 ?
Ans:- Therefore, in total there are 24 binary 1’s, so the subnet mask is /24.

## Slide 71: Example
200. 10. 20. 40/ 28 (28 number of 1’s network ID)
28 | 4
32 bits

## Slide 72: Question related to classless routing?
How many hosts are there?
Calculate network masks
To which N/w your IP belongs?

## Slide 73: Question related to classless routing?
How many hosts are there?
Calculate network masks
To which N/w your IP belongs?
200.10.20.40/28
28 | 4
32 bits
NetID
HostID
24 = 16 host

## Slide 74: Question related to classless routing?
How many hosts are there?
Calculate network masks
To which N/w your IP belongs?
200.10.20.40/28
28 | 4
32 bits
NetID
HostID
11111111.11111111.11111111.11110000
28 1’s network ID
4 host ID

## Slide 75: Question related to classless routing?
Convert these bits into mask
11111111.11111111.11111111.11110000
255. 255. 255. ?

## Slide 76: Question related to classless routing?
Convert these bits into mask
11110000
0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1* 27 | 1* 26 | 1* 25 | 1* 24 | 0* 23 | 0* 22 | 0* 21 | 0* 20
0
0
0
1
1
1
1

## Slide 77: Question related to classless routing?
Convert these bits into mask
11110000
0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1* 27 | 1* 26 | 1* 25 | 1* 24 | 0* 23 | 0* 22 | 0* 21 | 0* 20
128 | 64 | 32 | 16 | 0 | 0 | 0 | 0
0
0
0
1
1
1
1

## Slide 78: Question related to classless routing?
Convert these bits into mask
11110000
0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1* 27 | 1* 26 | 1* 25 | 1* 24 | 0* 23 | 0* 22 | 0* 21 | 0* 20
128 | 64 | 32 | 16 | 0 | 0 | 0 | 0
0
0
0
1
1
1
1
128+64+32+16 = 240

## Slide 79: Question related to classless routing?
11111111.11111111.11111111.11110000
Convert these bits into mask
255.255.255. 240 (final mask)
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1* 27 | 1* 26 | 1* 25 | 1* 24 | 0* 23 | 0* 22 | 0* 21 | 0* 20
128 | 64 | 32 | 16 | 0 | 0 | 0 | 0
128+64+32+16 = 240

## Slide 80: Question related to classless routing?
Find network ID
28 bits wont change
200.10.20.40/28
28 | 4
32 bits
200(this representing 8 bits)

## Slide 81: Question related to classless routing?
Find network ID
28 bits wont change
200. 10. 20. 40/28
200 . 10(representing 8 bits)
i.e. 8+8=16
28 | 4
32 bits

## Slide 82: Question related to classless routing?
Find network ID
28 bits wont change
200. 10. 20. 40/28
200 . 10. 20(representing 8 bits)
i.e. 8+8+8=24
We need 28
28 | 4
32 bits

## Slide 83: Question related to classless routing?
Find network ID
28 bits wont change
200. 10. 20. 40/28
200 . 10. 20. 00101000
i.e. 8+8+8=24
We need 28. we need 4 more bits to complete 28.
28 | 4
32 bits

## Slide 84: Question related to classless routing?
Find network ID
28 bits wont change
200. 10. 20. 40/28
200 . 10. 20. 00101000
i.e. 8+8+8=24
We need 28. we need 4 more bits to complete 28.
28 | 4
32 bits
We wont change network ID. 28 will complete now
4 representing host

## Slide 85: Question related to classless routing?
Find network ID
28 bits wont change
200. 10. 20. 40/28
200 . 10. 20. 00100000
i.e. 8+8+8=24
We need 28. we need 4 more bits to complete 28.
28 | 4
32 bits
4 representing host
All host bits will be converted into zero

## Slide 86: Question related to classless routing?
Find network ID
28 bits wont change
200. 10. 20. 40/28
200 . 10. 20. 00100000
200. 10. 20. 32/28
Network id or block id 32/28
28 | 4
32 bits
4 representing host

## Slide 87: Question related to classless routing?
We can do AND also with subnet mask
255.255.255.240
200. 10 . 20. 40
255. 10. 20 . 32/28
11110000
00101000
00100000 = 32

## Slide 88: CIDR
A person has to make sure that the masks are contagious, i.e. a subnet mask like 10111111.X.X.X can’t exist.

## Slide 89: CIDR
It is not necessary that the divider between the network and the host portions is at an octet boundary. For example, in CIDR a subnet mask like 255.224.0.0 or 11111111.11100000.00000000.00000000 can exist.

## Slide 90: Reserved addresses
There are a few reserved IPv4 address spaces which cannot be used on the internet. These addresses serve special purpose and cannot be routed outside the Local Area Network.

## Slide 91: Loop back address
The IP address range 127.0.0.0 – 127.255.255.255 is reserved for loopback, i.e., a Host’s self-address, also known as localhost address

## Slide 92: Link-local Addresses
In case a host is not able to acquire an IP address from the DHCP server and it has not been assigned any IP address manually, the host can assign itself an IP address from a range of reserved Link-local addresses. Link local address ranges from
169.254.0.0 -- 169.254.255.255.