## Slide 2
After this lecture you will be able to
  what is Unicast Routing.
  three major protocols for unicast routing.
  classification of Routing Algorithms.

## Slide 3: Unicast
Unicast means the transmission from a single sender to a single receiver.
It is a point to point communication between sender and receiver.
There are various unicast protocols such as
  TCP, HTTP, etc.

## Slide 4: Routing Protocol
Routing Protocol
Interdomain
Intradomain
Path Vector
BGP
Distance Vector
BGP
Link State
OSPF

## Slide 5: Types of Protocol
Three major protocols for unicast routing
Distance Vector Routing
Link State Routing
Path-Vector Routing

## Slide 6: Distance Vector Routing
The least-cost route between any two nodes is the route with minimum distance.
Each node maintains a vector(table) of minimum distances to every node.
The table at each node also guides the packets to the desired node by showing the showing the next hop routing.

## Slide 7: Distance Vector Routing
Example:
Assume each nodes as the cities. Lines as the roads connecting them.

## Slide 8: Final Distance Vector Routing Table

## Slide 9: Initialization
The table in figure are stable.
Each node knows how to reach any other node and their cost.
At the beginning, each node know the cost of itself and its immediate neighbor.[those node directly connected to it.]

## Slide 10: Initialization
Assume that each node send a message to the immediate neighbors and find the distance between itself and these neighbors.
The distance of any entry that is not a neighbor is marked as infinite (unreachable)

## Slide 11: Initialization of tables in distance vector routing (DVR)

## Slide 12: Sharing in distance vector routing (DVR)
How much of the table must be shared with each neighbor?
The third column of the table (next hop) is not useful for the neighbor.
When the neighbour receives a table, this column needs to be replaced with the sender's name.

## Slide 13: Sharing in distance vector routing (DVR)
If any of the rows can be used, the next node column filled with sender of the table.
Therefore, a node can send only the first two column of its table to any neighbor.

## Slide 14: Updating in distance vector routing example: C to A
A to A via C: ACA = AC+ CA = 2+2
A to B via C: ACB = AC + CB = 2+4
A to D via C: ACD = AC + CD = 2+ inf. A to E via C: ACD = AC + CE = 2+4
A to C via C: ACB = AC + CC = 2+0

## Slide 15: When to Share in distance vector routing (DVR)
Periodic Update: A node sends its table, normally every 30s, in a periodic update, it depends on the protocol that is using DVR.
Triggered Update: A node sends its two-column routing table to its neighbors anytime there is a change in its routing table.

## Slide 16: When to Share in distance vector routing (DVR)
This is called triggered update the change can result from the following:
A node receives a table from a neighbor, resulting in changes in its own table after updating.
A node detects some failure in the neighboring links which results in a distance change to infinity.

## Slide 17: Distance vector routing
3 keys to understand how this algorithm works:
  Sharing knowledge about the entire AS. Each router shares its knowledge about the entire AS with neighbours. It sends whatever it has.
  Sharing only with immediate neighbours. Each router sends whatever knowledge it has thru all its interface.

## Slide 18: Distance vector routing
  Sharing at regular intervals. sends at fixed intervals, e.g. every 30 sec.
  Problems: Tedious comparing/updating process, slow response to infinite loop problem, huge list to be maintained!!

## Slide 19: LINK State Routing

## Slide 20: Link State routing
If each node in the domain has the entire topology of the domain the list of nodes and links, how they are connected including the type, cost (metric), and condition of the links (up or down)-the node can use Dijkstra's algorithm to build a routing table.

## Slide 21: Link State Routing
A
C
B
E
D
A
B
C
E
D
A
B
C
E
D
A
B
C
E
D
A
B
C
E
D
A
B
C
E
D
5
4
2
3
4
3

## Slide 22: Link State Routing
The topology must be dynamic, representing the latest state of each node and each link.
If there are changes in any point in the network (a link is down, for example), the topology must be updated for each node.

## Slide 23: Link State Knowledge

## Slide 24: Link State routing
Link state table will be generated before routing table.
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
2
1

## Slide 25: Link State Routing
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
R1 | 
Seqno | 
TTL | 
R2 | 6
R3 | 3
Link state table for R1
2
1

## Slide 26: Link State Routing
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
R1 | 
Seqno | 
TTL | 
R2 | 6
R3 | 3
R3 | 
Seqno | 
TTL | 
R1 | 3
R2 | 2
R5 | 9
2
1
Link state table for R3

## Slide 27: Link State Routing
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
R1 | 
Seqno | 
TTL | 
R2 | 6
R3 | 3
R3 | 
Seqno | 
TTL | 
R1 | 3
R2 | 2
R5 | 9
2
1
Link state table for R5
R5 | 
Seqno | 
TTL | 
R3 | 9
R4 | 1
R6 | 4

## Slide 28: Link State Routing
R1 | 
Seqno | 
TTL | 
R2 | 6
R3 | 3
R3 | 
Seqno | 
TTL | 
R1 | 3
R2 | 2
R5 | 9
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
2
1
Link state table for R6
R3 | 
Seqno | 
TTL | 
R3 | 9
R4 | 1
R6 | 4
R6 | 
Seqno | 
TTL | 
R4 | 8
R5 | 4

## Slide 29: Link State Routing
R1 | 
Seqno | 
TTL | 
R2 | 6
R3 | 3
R3 | 
Seqno | 
TTL | 
R1 | 3
R2 | 2
R5 | 9
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
2
1
Link state table for R4
R3 | 
Seqno | 
TTL | 
R3 | 9
R4 | 1
R6 | 4
R6 | 
Seqno | 
TTL | 
R4 | 8
R5 | 4
R4 | 
Seqno | 
TTL | 
R2 | 7
R5 | 1
R6 | 8

## Slide 30: Link State Routing
R1 | 
Seqno | 
TTL | 
R2 | 6
R3 | 3
R3 | 
Seqno | 
TTL | 
R1 | 3
R2 | 2
R5 | 9
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
2
1
Link state table for R2
R5 | 
Seqno | 
TTL | 
R3 | 9
R4 | 1
R6 | 4
R6 | 
Seqno | 
TTL | 
R4 | 8
R5 | 4
R4 | 
Seqno | 
TTL | 
R2 | 7
R5 | 1
R6 | 8
R2 | 
Seqno | 
TTL | 
R1 | 6
R3 | 2
R4 | 7

## Slide 31: Sharing
Dissemination of LSPs to every other router, called flooding, in an efficient and reliable way.

## Slide 32: Link State Routing
At R1
R1
R2
R3
6
3
2

## Slide 33: Link State Routing
At R1, when R3 will share information
R1
R2
R3
R5
6
3
2
9

## Slide 34: Link State Routing
At R1->When R5 will share information
R1
R2
R6
R3
R5
6
4
3
2
1
R4

## Slide 35: Link State Routing
At R1->Similarly all with share information with R1.
Global Knowledge (not in distance vector routing).
R1
R2
R4
R6
R3
R5
6
7
8
4
3
2
1
Next step is single source shortest path(Dijkstra Algorithm)

## Slide 36: Working of Dijstra Algorithm
R1 | R2 | R3 | R4 | R5 | R6
 | 6 | 3 | ∞ | ∞ | ∞
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
2
1

## Slide 37: Working of Dijstra Algorithm
R1 | R2 | R3 | R4 | R5 | R6
 | 6 | 3 | ∞ | ∞ | ∞
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
Minimum Distance is R3, So
R1,R3 will become source

## Slide 38: Working of Dijstra Algorithm
R1 | R2 | R3 | R4 | R5 | R6
 | 6 | 3 | ∞ | ∞ | ∞
R1,R3 | 5 |  | ∞ | 12 | ∞
R1,R3,R2 |  |  | 12 | 12 | ∞
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
2
1

## Slide 39: Working of Dijstra Algorithm
R1 | R2 | R3 | R4 | R5 | R6
 | 6 | 3 | ∞ | ∞ | ∞
R1,R3 | 5 |  | ∞ | 12 | ∞
R1,R3,R2 |  |  | 12 | 12 | ∞
R1,R3,R2,R4 |  |  |  | 12 | 21
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
2
1

## Slide 40: Working of Dijstra Algorithm
R1 | R2 | R3 | R4 | R5 | R6
 | 6 | 3 | ∞ | ∞ | ∞
R1,R3 | 5 |  | ∞ | 12 | ∞
R1,R3,R2 |  |  | 12 | 12 | ∞
R1,R3,R2,R4 |  |  |  | 12 | 21
R1,R3,R2,R4 ,R5 |  |  |  |  | 16
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
2
1

## Slide 41: Will make routing table
R1 | 0
R2 | 5
R3 | 3
R4 | 12
R5 | 12
R6 | 16
R1 | R2 | R3 | R4 | R5 | R6
 | 6 | 3 | ∞ | ∞ | ∞
R1,R3 | 5 |  | ∞ | 12 | ∞
R1,R3,R2 |  |  | 12 | 12 | ∞
R1,R3,R2,R4 |  |  |  | 12 | 21
R1,R3,R2,R4,R5 |  |  |  |  | 16

## Slide 42: Will make routing table
R1 |  | Next Node
R1 | 0 | R1
R2 | 5 | R1
R3 | 3 | R1
R4 | 12 | R3,R2
R5 | 12 | R3
R6 | 16 | R3,R5
R1
R2
R4
R6
R3
R5
6
7
8
4
9
3
2
1

## Slide 43: Path Vector Routing

## Slide 44: Path Vector Routing
Distance vector and link state routing are both intradomain routing protocols.
They can be used inside an autonomous system, but not between autonomous systems.

## Slide 45: Path Vector Routing
These two protocols are not suitable for interdomain routing mostly because of scalability.
Path vector routing proved to be useful for interdomain routing

## Slide 46: Path
It is an exterior routing protocol provided to be useful for inter-domain or inter- As routing.
In this routing, a router has a list of n/w’s that can be reached with the path to reach each one.
As the name suggests,it tells the path.

## Slide 47: Reachability
A4,B4 and C1 are a speaker nodes.
Speaker nodes will communicate with another
In each autonoumous system, each speaker node maintain routing table
A2
A1
A3
A4
B1
B3
B2
B4
C1
C2
C4
C3
AS1
AS2
AS3

## Slide 48: Reachability
A2
A1
A3
A4
B1
B3
B2
B4
C1
C2
C4
C3
Routing table of A4 | 
Destination | Path
A1 | As1
A2 | As1
A3 | As1
A4 | As1

## Slide 49: Path Vector routing
Routing tables:
  A path vector routing for each router can be created if ‘AS’ share their reachability list with each other.
Destination | Path
A1 | AS1
A2 | AS1
A3 | AS1
A4 | AS1
B1 | AS1-AS2
B2 | AS1-AS2
B3 | AS1-AS2
B4 | AS1-AS2
Destination | Path
C1 | AS1-AS3
C2 | AS1-AS3
C3 | AS1-AS3
C4 | AS1-AS3

## Slide 50: Path Vector routing
Loop prevention
  The instability of distance vector routing and the creation of loops can be avoided in path vector routing.
  When a router receives a message, it checks to see if its autonomous system is in the path list to the destination.
  If it is, looping is involved and the message is ignored.

## Slide 51: Routing Algorithm
Routing is process of establishing the routes that data packets must follow to reach the destination.
In this process, a routing table is created which contains information regarding routes which data packets follow.

## Slide 52: Classification of Routing Algorithms
Classification of Routing Algorithms
Adaptive Algorithms
Isolated
Centralized
Distributed
Non-Adaptive Algorithms
Flooding
Random walk

## Slide 53: Comparison
Routing | Flooding
Routing table is required | No routing table is required
May give shortest path | Always gives shortest path
Less reliable | More reliable
Traffic is less | Traffic is high
No duplicate packets | Duplicate packets are present