## Slide 2
After this lecture you will be able to
  learn the architecture of OSI model.
  understand the layers of OSI model and their functions.

## Slide 3: Layered Tasks
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.
Topics discussed in this section: Sender, Receiver, and Carrier Hierarchy.

## Slide 4: Tasks involved in sending a letter
The letter is written, put in an envelope, and dropped in a mailbox.
The letter is carried from the post office to the mailbox
The letter is picked up, removed from the envelope; and read
The letter is carried from the mailbox to a post office.
The letter is delivered to a carrier by the post office.
The letter is delivered from the carrier to the post office
Higher layers
Middle layers
Lower layers
The parcel is carried from the source to the destinations
Sender
Reciever

## Slide 5: The OSI Model
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
Topics discussed in this section: Layered Architecture, Peer-to-Peer Processes, Encapsulation.

## Slide 6: OSI Model
OSI is the model
ISO is the organization

## Slide 7: Seven layers of the OSI model
Application
Presentation
Session
Transport
Network
Data link
Physical
1
2
3
4
5
6
7

## Slide 8: The Interaction between Layers in the OSI Model

## Slide 9: An exchange using the OSI model

## Slide 10: Application Layer

## Slide 11: Specific Services Provided by the Application Layer
Network virtual Terminal
File transfer, access, and management.
Mail services.
Web Surfing

## Slide 12: Specific Services Provided by the Application Layer
Network virtual Terminal
TELNET

## Slide 13: Specific Services Provided by the Application Layer
File transfer, access, and management.
FTP

## Slide 14: Specific Services Provided by the Application Layer:
Mail services
Sender
Internet
SMTP
SMTP
SMTPPOP3 / IMAP
Sender’s Mail Server
Receiver’s Mail Server
Receiver

## Slide 15: Web Surfing

## Slide 16: NOTE
The application layer is responsible for providing services to the user.

## Slide 17: Presentation Layer
Presentation layer
Application Layer

## Slide 18: Presentation layer
What is the format of data?

## Slide 19: Presentation Layer
Specific responsibilities of the presentation layer includes-
  Translation
  Encryption
  Compression

## Slide 20: Translation
101011100011100011000
Convert
Example conversion of ASCII to EBCDIC

## Slide 21: Data compression
Presentation layer used to reduce the data before transmission that is known as Data compression.
That can be Lossy and Lossless compression.

## Slide 22: Data Compression
Data Compression
Lossless Data
Compression
Lossy Data
Compression

## Slide 23: Encryption and Decryption

## Slide 24: Note
The presentation layer is responsible for translation, compression, and encryption.

## Slide 25: Session layer
Dialog Control
Authentication and Authorization
Session management
Synchronization

## Slide 26: Session Layer
Party

## Slide 27: Session Layer
Setting up

## Slide 28: Session Layer
Assisting

## Slide 29: Session Layer
Cleaning

## Slide 30: Same case with Session Layer
Helping to setting up connection
Dialog control

## Slide 31: Same case with Session Layer
APIs NETBIOS
Helping to setting up connection
APIs NETBIOS

## Slide 32: Authentication and Authorization
Authentication
Authorization
Who are you?
What permissions do you have?
VS

## Slide 33: Authentication and Authorization

## Slide 34: Session Management

## Slide 35: Synchronization
System sending a file of 2000 pages

## Slide 36: Synchronization
After 100 pages

## Slide 37: Note
The session layer is responsible for dialog control and synchronization.

## Slide 38: Transport layer
Segmentation and reassembly
Flow control
Error Control
Service point addressing

## Slide 39: Segmentation and Reassembly
Session layer
Transport Layer

## Slide 40: Segmentation and Reaasembly
Session layer
Transport Layer
Data Unit
Data Unit
Data Unit
Segments

## Slide 41: Segmentation and Reassembly
Sequence no. and port number
data unit
Segments
Sequence no. and port number
data unit
Sequence no. and port number
data unit

## Slide 42: Segmentation and Reassembly
Sequence no. and port number
data unit
Sequence no. and port number
data unit
Sequence no. and port number
data unit

## Slide 43: Segmentation and Reassembly
Reassemble segments
Application Layer
Data
Segment 2
Segment 1
Segment 3

## Slide 44: Flow Control
100Mbps
10Mbps
50Mbps

## Slide 45: Error Control
Automatic repeat request
Data Unit
Data Unit
Data Unit
Data Unit
Data Unit
Missing

## Slide 46: Error Control
Automatic repeat request
Data Unit
Data Unit
Data Unit
Data Unit
Data Unit
Checksum
Data Unit
Checksum
Checksum
Checksum
Corrupted

## Slide 47: Protocols of Transport Layer
TCP | UDP
Connection Oriented transmission | Connectionless transmission
TCP is slower | UDP is faster
Acknowledgment | No Acknowledgment
Used where full data delivery is must | Does not matter whether we gave received all data

## Slide 48: Service point addressing
Internet
Network layer
Host-to-host delivery
Transport layer
Process-to-process delivery
Process
Process

## Slide 49: Note
The transport layer is responsible for the delivery of a message from one process to another.

## Slide 50: Network Layer
Logical Addressing
Routing

## Slide 51: Logical Addressing
Transport layer
Network Layer
Segments

## Slide 52: Logical Addressing
Ipconfig command

## Slide 53: Logical Addressing
Transport Layer
Network Layer
Network 1
Network 2
Segment
IP1 IP2
IP 1
IP 2
Packets
Segment
Sender
Receiver

## Slide 54: Routing

## Slide 55: Note
The network layer is responsible for the delivery of individual packets from the source host to the destination host.

## Slide 56: Data Link Layer
Network layer
Data Link Layer
Data Link layer receives data packet from network layer. Data packets contains IP address of sender and receiver.

## Slide 57: Data Link Layer
Framing
Physical addressing
Flow control.
Error control
Access control.

## Slide 58: Physical Addressing
If frames are to be distributed to different systems on the network, DataLink layer adds header to the frame.

## Slide 59: Types of Addressing
Types of Addressing
Physical addressing
Logical addressing

## Slide 60: Types of Addressing
Types of Addressing | 
Logical Addressing | Physical addressing
Done at Network layer | 
Sender and receiver IP addressing are assigned to each segment to form a data packet

## Slide 61: Types of Addressing
Types of Addressing | 
Logical Addressing | Physical addressing
Done at Network layer | Done at Data Link Layer

## Slide 62: Types of Addressing
Types of Addressing | 
Logical Addressing | Physical addressing
Done at Network layer | Done at Data Link Layer

## Slide 63: Types of Addressing
Types of Addressing | 
Logical Addressing | Physical addressing
Done at Network layer | Done at Data Link Layer
Network Interface card
Network Interface card

## Slide 64: Types of Addressing
Local media includes

## Slide 65: Flow Control
Data link layer imposes a flow control mechanism to avoid overwhelming the receiver.

## Slide 66: Error Control
Adds reliability to the physical layer by adding mechanisms
Detect and retransmit damaged or lost frames.
Recognize duplicate frames.
Normally achieved through a trailer added to the end of the frame.

## Slide 67: Access Control
Data link layer keeps an eye when shared media is Free that device can send data. This is called CSMA.

## Slide 68: Note
The data link layer is responsible for moving frames from one hop (node) to the next.

## Slide 69: Physical layer
Transport layer
Network layer
  1000101010101000111000000(Bits)
Signals
Media
Data link layer

## Slide 70: The physical layer is also concerned
Data rate
Synchronization of bits
Physical topology
Transmission mode

## Slide 71: Note
The physical layer is responsible for movements of individual bits from one hop (node) to the next.

## Slide 72: Summary
Application
Presentation
Session
Transport
Network
Data link
Physical
To allow access to network resources
To establish, manage, and terminate sessions
To move packets from source to destination; to provide internetworking
To transmit bits over a medium; to provide mechanical and electrical specifications
To organize bits into frames; to provide hop-to-hop delivery
To provide reliable process-to-process message delivery and error recovery
To translate, encrypt, and compress data

## Slide 73: Protocol Data Unit (PDU)
Data
Application
Presentation
Session

## Slide 74: Protocol Data Unit (PDU)
Data
Application
Presentation
Session
Transport
Segments

## Slide 75: Protocol Data Unit (PDU)
Data
Application
Presentation
Session
Transport
Network
Segments
Packets

## Slide 76: Protocol Data Unit (PDU)
Data
Application
Presentation
Session
Transport
Network
Data link
Segments
Packets
Frames

## Slide 77: Protocol Data Unit (PDU)
Data
Application
Presentation
Session
Transport
Network
Data link
Physical
Segments
Packets
Frames
10101100